## Slide 1: Warm Up: 3/11 Name one thing you learned in the theatre the last 2 Days
Obj: SWBAT differentiate between different parts of a light

## Slide 2: Parts of a Light
Every lighting fixture contains a lamp (bulb), reflector and sometimes a lens.
Parcans do not have a lens

## Slide 3: Parts of a Lighting Fixture
Lamp Housing – Back of fixture that holds the lamp (the bulb)
C-Clamp – Metal bracket that holds the fixture to the pipe or batten
Yoke – U-Shaped bracket which connects the C-Clamp to the fixture
Safety Cable – Goes around the fixture and the pipe as a back up
Shutter Handle – Controls the shutters to change the shape of the light
Power Cable - What you plug in
Gel Frame Holder – Holds the gel which creates the color

## Slide 4: C – Clamp Close Up
Crescent wrenches are used to tighten or loosen all the bolts around a fixture.
The ½ Bolt under the yoke is called the “Jesus” nut
NEVER loosen the “Jesus Nut” to rotate the fixture
To rotate fixture use the Pivot Locking Bolt

## Slide 5: Ways of Hanging Lights
Batten – Standard lighting pipe (also known as Electrics if they have electricity run through them)
Ladder – Hung from the ceiling or a batten they hang down and are often used for side light
Tormentors – Are hung off a wall (Sometimes called Booms)
Booms – Are a free standing pipe with a waited bottom (Sometimes called trees)
Stands – An area to rest a light with a waited bottom

## Slide 6: Types of Plugs
Edison – standard wall plug
Stage Pin – Three prongs
Twist Lock – plug is twisted to secure. What we have here

## Slide 7: Safety and Handling Rules
Always use gloves
  Fixtures get hot so the gloves protect your hands from the heat
  Stronger grip
  Keeps your hands clean

## Slide 8: Safety and Handling Rules
Never NEVER touch the lamp (bulb) by the glass
  Oils on your hands transfer to the lamp
  Oil heats up hotter than the surface of the lamp
  Creates a weak point on the lamp so the lamp would go “boom” and explode

## Slide 9: Safety and Handling Rules
Always attach the safety cable first
  Safety cables are rated for a few hundred pounds
  Back up device to catch lamp from falling if improperly hung
  Source 4’s weight 14 pounds + landing on your head = Dead

## Slide 10: Safety and Handling Rules
Always secure your wrench to your belt/pants
  Wrench is always within arms reach
  If you drop the wrench it won’t fall therefore causing:
    You to have to go get it
    Landing on a set piece breaking it
    Landing on a person and breaking them

## Slide 11: Safety and Handling Rules
Call out when “Going Dark” aka turning off lights
  Gives everyone on stage a heads up that the lights are turning off
Also call things like:
  Flys coming in or out
  Electrics coming in or out
  Loud Noises

## Slide 12: Price Break Down
The fixtures to the left are standard ERS lights from two different companies
These are the same Source 4 ERS, but as LED Source 4s…note they are about 10 times more expensive

## Slide 13: Fresnels, Parcans and Source 4 Pars:

## Slide 14: And for fun…